## Slide 2: Pseudohypacusis/ Nonorganic/ Functional Hearing Loss:
What do you do when someone shows a hearing loss you don't think is true?

## Slide 3
Fahimeh Hajiabolhassan
2020

## Slide 4: Nonorganic HL
Psychogenic-
Psychogenic HL
Functional HL
Psedohypoacausis
Nonorganic HL
Malingering
  .

## Slide 5: Malingering:
Often in compensation cases
  Industrial
  Military
In children, to get attention
  Most often ages 10 to 12

## Slide 6: Inconsistencies
Behavior vs. test results
SRT vs. PTA
Air-Bone Gap and Type A tympanogram
No Shadow Curve

## Slide 7: Malingering
Case history
Ascending Desending Method
Duration
90 deg.
Hand

## Slide 8: Tests for pseudohypacusis:
The Stenger Test
Delayed Auditory Feedback tests
Swinging Story Test
ABR
Bekesy Audiometry

## Slide 9: The Stenger Test:
for use in unilateral HL
Based on the STENGER EFFECT:
If a listener is presented with the same stimulus in each ear, she will only hear the tone in the ear in which it is louder.

## Slide 10: The Stenger Test (cont’d)
tone 10 dB SL in better ear, -10 in poorer, if no response: caught
Right ear AC T=50 ,left ear AC T=10
Stenger Test :Right ear AC =40 ,left ear AC=20

## Slide 11: The Stenger Test (cont’d)
Minimum Contralateral Interference Level(MCIL): Lowest level at which you can get the Stenger Effect, usually within 20 dB of real threshold.
Right ear AC T=50 ,left ear AC T=10
MCIL:Right ear AC =0 ,left ear AC=20

## Slide 12: The Stenger Test (cont’d)
tone 10 dB SL in better ear, -10 in poorer, if no response: caught
Minimum Contralateral Interference Level: Lowest level at which you can get the Stenger Effect, usually within 20 dB of real threshold.
Speech Stenger is like pure-tone although using SRT

## Slide 13: Delayed Speech Feedback Test:
person speaks into microphone
output of mic is delayed (100-200 ms)
seek level where DAF produces difficulty in speaking.

## Slide 14: Pure-tone DAF Test:
Called “Tone Tap Test”
Ask person to tap a pattern over and over
beep delivered to the ear with each tap (with a delay)
level of beep is raised until pattern changes

## Slide 15: Swinging Story Test:
to catch a unilateral loss.
Story switches from one ear to both and to the other ear
Two possible meanings:
--one if you hear whole story
--other if you hear only what is in both ears or in good ear

## Slide 16: Bekesy audiometry:
Looking for Type V
Person is trying to respond at a consistent loudness
Continuous tone produces greater loudness than the interrupted tone
So, Cont gives lower thresholds//Inter gives higher thresholds

## Slide 17: Yes-No test
Children
5 dB

## Slide 18: Low level phonetically balanced word test
SDS
5 dBsl= 25%
40 dBsl= 100%

## Slide 19: Electrophysiological Tests: ABR
“Objective” Assessment of hearing
Beware higher level disorders, (e.g., Cortical).

## Slide 20: Electrophysiological Tests: Acoustic Reflexes
VERY LOW SL’s--suspect malingering
SPAR-- Sensitivity Prediction from the Acoustic Reflex
based on changes in AR thresh with increasing stimulus bandwidth.

## Slide 21: Doerfler-Stewart Test:
based on the effect of masking on the SRT.

## Slide 22: Lombard Test:
Raising of voice in presence of noise.
Not a greatly sensitive or specific test.