## Slide 2: Pseudohypacusis/ Nonorganic/ Functional Hearing Loss:

## Slide 3
Fahimeh Hajiabolhassan
2020

## Slide 4: The Stenger Test:
for use in unilateral HL
Based on the STENGER EFFECT:
If a listener is presented with the same stimulus in each ear, she will only hear the tone in the ear in which it is louder.

## Slide 5: The Stenger Test (cont’d)
tone 10 dB SL in better ear, -10 in poorer, if no response: caught
Right ear AC T=50 ,left ear AC T=10
Stenger Test :Right ear AC =40 ,left ear AC=20

## Slide 6: The Stenger Test (cont’d)
Minimum Contralateral Interference Level(MCIL): Lowest level at which you can get the Stenger Effect, usually within 20 dB of real threshold.
Right ear AC T=50 ,left ear AC T=10
MCIL:Right ear AC =0 ,left ear AC=20

## Slide 7: The Stenger Test (cont’d)
tone 10 dB SL in better ear, -10 in poorer, if no response: caught
Minimum Contralateral Interference Level: Lowest level at which you can get the Stenger Effect, usually within 20 dB of real threshold.
Speech Stenger is like pure-tone although using SRT

## Slide 8: Delayed Speech Feedback Test:
person speaks into microphone
output of mic is delayed (100-200 ms)
seek level where DAF produces difficulty in speaking.

## Slide 9: Pure-tone DAF Test:
Called “Tone Tap Test”
Ask person to tap a pattern over and over
beep delivered to the ear with each tap (with a delay)
level of beep is raised until pattern changes

## Slide 10: Swinging Story Test:
to catch a unilateral loss.
Story switches from one ear to both and to the other ear
Two possible meanings:
--one if you hear whole story
--other if you hear only what is in both ears or in good ear